## Slide 1: Herding the Elephants Detecting Network-Wide Heavy Hitters with Limited Resources
Yannick Merkli, Tim Bohren, Felix Rüssli
Advisor: Albert Gran Alcoz
Supervisor: Laurent Vanbever

## Slide 2
Network operators need to effectively separate small flows from large flows
Detect Denial-of-Service attacks
Optimize network by detecting congestion and failures
Usage based pricing

## Slide 3: Just measure each flow on the switch…
Heavy hitters exceed some threshold of packets or bytes
Network switches are constrained in memory and computation
  Measuring each flow is infeasible
Prior work focused heavy hitter detection on a single switch under these constraints
Flow | count
 | 10
 | 30
 | 105
Flow | count
 | 10
 | 30
 | 105
> 100

## Slide 4: Reality is more complicated
Real networks consist of multiple ingress switches
Heavy hitters are often network-wide
  Heavy hitter detection on a single switch is not enough
We need coordination among network switches for network-wide detection
Flow | count
 | 80
Flow | count
 | 80
Flow | count
 | 90
Flow | count
 | 90
Flow | count
 | 95
Flow | count
 | 95
Detect flows with count > 100
remains undetected although exceeding the threshold
Herd tries to solve network-wide detection under resource constraints

## Slide 5: Herd is a distributed technique to detect network-wide heavy hitters under resource constraints
Ingress switches
Coordinator
Communication
use probabilistic sample-and-hold for flows → less switch memory
probabilistically report to the coordinator → less communication overhead
combines partial information to attain a global view of the network
detects heavy hitter flows

## Slide 6: Who’s who in the Zoo
Elephant flows: heavy hitters
  number of reports exceeded
  report threshold R
Mule flows: exceed the mule threshold
  switch sends report to coordinator with
  report probabiliy r
Mole flows: flows sampled by the switch
  switch counts number of packets with
  sampling probability s
Mouse flows: small and numerous
  not counted at the switch
mouse
mole
mule
elephant
central coordinator
local ingress switch

## Slide 7: Most flows exhibit spatial locality
Flows often exhibit preference for certain ingress switches
The fewer flows an ingress switch observes, the higher the threshold must be
Flows are put into groups
  src, dst are /8 subnets
Coordinator tracks : number of switches that observe at least one flow
Mule threshold and report probability are adapted based on locality

## Slide 8: Ingress switches probabilistically sample and report flows
Data plane (P4)
Stores in match-action table
  in case of table miss, send a hello via copy-to-cpu
Counts packets of a flow with probability s
  Stored in a multi-stage hash table
Sends a report (via copy-to-cpu) with probability if exceeds
Control plane (Python)
Sends hellos and reports to coordinator by invoking remote procedure calls
Receives locality parameter via callback
Calculates and writes into match-action table
Group values MAT
Flow count table
copy-to-cpu
Data plane
table_add
unpack
Control plane

## Slide 9: What if the multi-stage hash table is full?
Original paper
All flows that don’t fit are sent to the coordinator
  Paper doesn’t specify what the coordinator should do with them
  Overloads the network the messages
Our solution
Notify the controller as soon as hash tables are full
  Controller will reset all tables
What about accuracy?
Packet count is reset after every report
Large flows get reported several times
  resetting the hash table corresponds to losing one report
  → reasonable, since the report threshold

## Slide 10: Coordinator tracks locality and number of report per flow
Server with an exposed RPC service for sending hellos and reports
Combines partial information to calculate and store locality parameters
Dynamically updates on switches via callback functions
Tracks the number of reports for each flow f
  Detects heavy hitters based on report threshold R
Locality table
Report counts
label as heavy hitter
Coordinator

## Slide 11: Ingress switches communicate with the coordinator
f
Coordinator
group values MAT
external
internal
Flow f of unknown group g arrives
  group values MAT miss!
sends to coordinator
Coordinator sends to
stores in MAT
f is sampled with probability s
Packet count
  sends with probability
Coordinator receives several
  f is a heavy hitter
g
Multi-stage hash table
f
f
f
f

## Slide 12: The evaluation topology is representative of a wide-area network
sends traffic towards
  400’000 packets using tcpreplay
  CAIDA anonymized internet packet trace
  Limited sending rate (300pps) due to mininet constraints
Load balancer distributes flow packets over two ingress switches (flow locality)
  based on the source IP
Ingress switches run Herd

## Slide 13: Herd(s=0.1) achieves the same detection accuracy as a protocol that samples every flow (s=1.0)
Herd(s=0.1) achieves 87% F1 score
Herd(s=1.0) achieves 86% F1 score
  needs 10x more switch memory than Herd(s=0.1)
Successfully proves that Herd works under switch memory constraints
The decrease in precision can be explained with the static report threshold R

## Slide 14: Herd achieves maximal detection accuracy for an approximation factor
The approximation factor determines the mule threshold:
Smaller → more reports → more communication
Proves that Herd works under communication constraints

## Slide 15: Challenges
Limited sending rate
Delay between sending a hello to writing to MAT
Load balancer started dropping packets at 400pps
Original paper
Often vague and omits crucial details
Authors stress importance of tuning parameters, but their algorithm is flawed
Notes: Speed issue in 3 points (3 types of delay), whole sentences

## Slide 16: Conclusion
We were able to reproduce the main claims of Herd, namely it working under resource constraints.
Future work
Improve parameter tuning
Dynamically adjust parameters

## Slide 17: Demo

## Slide 18: Questions?

## Slide 19: Herding the Elephants Detecting Network-Wide Heavy Hitters with Limited Resources
Yannick Merkli, Tim Bohren, Felix Rüssli
Advisor: Albert Gran Alcoz
Supervisor: Laurent Vanbever

## Slide 20: Herding the Elephants Detecting Network-Wide Heavy Hitters with Limited Resources
Yannick Merkli, Tim Bohren, Felix Rüssli
Advisor: Albert Gran Alcoz
Supervisor: Laurent Vanbever

## Slide 21: Herding the Elephants Detecting Network-Wide Heavy Hitters with Limited Resources
Yannick Merkli, Tim Bohren, Felix Rüssli
Advisor: Albert Gran Alcoz
Supervisor: Laurent Vanbever